## Slide 1
Design and Implementation of a Wireless Fall Detection Network Prototype using MEMS sensors
Ho Ngoc Khang Minh - Matriculation number: 1148602
1st Supervisor: Prof. Dr. –Ing Kira Kastell
2nd Supervisor: Dipl –Ing. Mohammad Reza Mansooji
Frankfurt am Main, September 2018

## Slide 2: AGENDA
Introduction to falls
Causes and consequences of falls
Literature Review
Objectives
Methodology and Algorithm
System Intergration
Data collection
Result
Discussion

## Slide 3: Introduction to falls
1 in 3
65 years older
fall once per year
Every 19 minutes
ONE
faller dies
hip fracture
200 falls result in

## Slide 4: Causes of a fall
Intrinsic factors
  Cognitive Impairment
  Postural control
  Cardiovascular problem
Extrinsic factors
  Dim lighting or glare
  Bad staircase design

## Slide 5: Consequences of falls
Physical consequences
  Hip fractures
    - A quarter million hip fractures occur each year
    Half of them cannot live independently
    $3 billions for medical treatment
  Head Injuries
  - 10 – 15% admission to the hospital because of head injuries caused by falls
  Death
  - 36.8 / 100 000 people die every year because of falls

## Slide 6: Consequences of falls
Psychological consequences
  Fear of falling again prevents them from their daily activity
  Stop going out or physical activities
  Increase the risk of falling because of physical function attenuation

## Slide 7: Literature Review
Existing Commercial Devices
  - Including one base station & one neck pendant
  - When detecting a fall, if the patient need help, not press the button
  - Automatically contact with monitoring center
  - $44.95 / month
Fig 1. Medical Guadian Fall Alert System

## Slide 8: Literature Review
Existing Commercial Devices
  - Detect fall
  - Monitoring heart rate
  - Sleep/wake pattern
  - Location of patient
  - $41.95 / month
Fig 2. myHalo Medical Alert System

## Slide 9: Literature Review
Existing Research
  - From Qiang Li and colleagues
  - Including one gyroscope and one accelerometer
  - Combine data from both sensor
  - Difficulty in differentiate jumping into bed and
  falling against a wall
Fig 3. Tempo 3.0 sensor node

## Slide 10: Literature Review
Existing Research
  - From Binh Nguyen & Tomkun
  - Using only one accelerometer
  - Automatically call 911 when detecting
  a fall
  - Visual LED indicator
  - Some action cannot be distinguished by
  propose algorithm
Fig 4. Product of Binh Nguyen’s group

## Slide 11: Project objective
Design a falling detection network
Sending alert signal to care-givers
1
2

## Slide 12: Methodology & Algorithm
Normalized Acceleration
where Ax, AY, Az represent acceleration in three directions
Normalized Angular Velocity
where represent angular velocity in three direction

## Slide 13: Algorithm
Lower fall threshold (LFT): local minima for the Acc resultant of each recorded activity are referred to as the signal lower peak values (LPVs).
Upper fall threshold (UFT): local maxima for the Acc and resultant of each recorded activity are referred to as the signal upper peak values (UPVs)

## Slide 14: Algorithm
3 Threshold Types
LFTAcc : lower limit for acceleration
UFTAcc : upper limit for acceleration
UFTGyro: upper limit for angular velocity

## Slide 15: Algorithm
*Nominated by Quoc T. Huynh et. al. [1]

## Slide 16: System Overview

## Slide 17: SENSORS
Inertia Measurement Unit (IMU) - MPU6050
Accelerometer
full-scale range of ±2g, ±4g, ±8g,
and ±16g.
Gyroscope
full-scale range of ±250, ±500, ±1000,
and ±2000 °/sec (dps)
Fig 5. MPU-6050 sensor

## Slide 18: DATA FUSION
Sensors Characteristics
  Accelerometer
Sensitive with any sudden small force
Data is reliable in long term
  Gyroscope
Drift over time
Give accurate information, not affected by
external force
Fig 5. MPU-6050 sensor

## Slide 19: MICRO-CONTROLER
ESP8266EX
- L106 32-bit RISC processor
- Maximum clock speed 160Mhz
- Supports GPIO, UART, I2C, ADC, etc.
- 50kB RAM and 16MB SPI flash
Fig 5. ESP8266EX

## Slide 20: POWER SUPPLY
ESP8266 Power Supply Shield

## Slide 21: COMMUNICATION
ESP8266EX with intergrated Wi-Fi module
- Full 802.11 b/g/n WLAN MAC standard
- Low power architecture
- Only 20in deep-sleep mode
- Power consumption: 1mW
- Support TCP protocol
Fig 5. ESP8266EX

## Slide 22: COMMUNICATION

## Slide 23: SOFTWARE

## Slide 24: Testing Method

## Slide 25: Results

## Slide 26: Further Development Machine Learning method Mobile Platform Pre-fall prediction
Improve the correct of falling detection with a bunch of training data set
Use integrated sensors on the smart phone to make it easy for you user to carry with them
Use modern technique in machine learning to predict whether patient will fall or not
01
02
03

## Slide 27: Reference
[1] Quoc T. Huynh, Uyen D. Nguyen, Lucia B. Irazabal, Nazanin Ghassemian, and Binh Q. Tran, “Optimization of an Accelerometer and Gyroscope-Based Fall Detection Algorithm”, Journal of Sensors.
[2] J. G.-A. Pedro Rodrigues, "Fall detection systems to be used by elderly people," in Handbook of Research on ICTs for Human-Centered Healthcare and Social Care, p. 87.J. G.-A. Pedro Rodrigues, "Fall detection systems to be used by elderly people," in Handbook of Research on ICTs for Human-Centered Healthcare and Social Care, p. 87.
[3]A. Bueno-Cavanillas, F. Padilla-Ruiz, J. J. Jimenez-Mole ´ on, ´C. A. Peinado-Alonso, and R. Galvez-Vargas, “Risk factors in ´falls among the elderly according to extrinsic and intrinsic precipitating causes,” European Journal of Epidemiology, vol. 16, no. 9, pp. 849–859, 2000.

## Slide 28: Thank you.